# (Your Business Name Here) – Safe Work Procedure

# WALK BEHIND ROTARY CULTIVATOR (PETROL)

DO NOT use this machine unless you have been instructed

in its safe use and operation and have been given permission

## PERSONAL PROTECTIVE EQUIPMENT

## PRE-OPERATIONAL SAFETY CHECKS

Locate and ensure you are familiar with all machine operations and controls.

Ensure all guards are fitted, secure and functional. Do not operate if guards are missing or faulty.

Check for loose/missing nuts, bolts and screws. Tighten and/or replace as needed.

Look for signs of damage to tillage tines. Replace if required.

Inspect fuel lines, tank and area around carburetor for fuel leaks. Do not operate if leaks are found.

## OPERATIONAL SAFETY CHECKS

Watch for ejected material. Ensure no person or animal is endangered when operating.

Adjust the handles to a position for comfort and good balance.

Set the tine depth according to soil conditions and the operator’s manual.

Ensure the cultivator is securely held and is on firm and even ground before starting.

Keep clear of rotating machine parts while the engine is operating.

Maintain a straight wrist position. Avoid using your wrist in a bent, extended or twisted position.

Be alert for rocks and other obstructions when operating the rotary hoe.

Take care when reversing or pulling the machine towards you.

Shut down immediately if the unit starts to shake or vibrate. Do not operate until the problem is corrected.

Always stop the engine and disconnect the spark plug wire before cleaning the tines or doing maintenance work.

Take care when refuelling to avoid spilling fuel onto hot motor or exhaust.

## CLEANING UP

Remove any foreign material from in and around the motor, tines and guards.

Keep the work area and implement shed in a safe, clean and tidy condition.

## POTENTIAL HAZARDS

Trip hazards.

Noise.

Foot injuries.

Hair/clothing getting caught in moving machine parts.

Flying debris.

## DON’T

Do not use faulty equipment. Immediately report suspect machinery.

This SWP does not necessarily cover all possible hazards associated with this equipment and should be used in conjunction with other references.  It is designed as a guide to be used to compliment training and as a reminder to users prior to equipment use.

This information is based on material published by the South Australian Department of Education and Children’s Services.