# (Your Business Name Here) – Safe Work Procedure

# CHAINSAW - ELECTRIC

DO NOT use this machine unless you have been instructed

in its safe use and operation and have been given permission

## PERSONAL PROTECTIVE EQUIPMENT

## PRE-OPERATIONAL SAFETY CHECKS

Locate and ensure you are familiar with all machine operations and controls.

Ensure all guards are fitted, secure and functional. Do not operate if guards are missing or faulty.

Ensure the machine and extension cord are tagged and are current.

Ensure the extension cord is in good condition and fully uncoiled.

Ensure a tagged and tested RCD is used when operating the machine. Trip test the RCD before use.

Ensure the chain guard and chain brake are functioning.

Ensure the chain is sharp and correctly tensioned.

Ensure the safety harness, if required, is in sound condition.

## OPERATIONAL SAFETY CHECKS

Maintain a proper balance and secure footing.

Keep a firm grip on the chainsaw with both hands and the thumb of the hand holding the front handle wrapped around the handle.

Start the cut with the saw chain rotating at full speed and the spiked bumper in contact with the wood.

Pay full attention to the operation and be alert for movement of the material being cut.

Be aware of the guidebar nose at all times when the saw chain is in motion.

Be alert to situations that may cause material to pinch the top of the saw chain.

Ensure no person or animal is endangered when operating equipment.

## ENDING OPERATIONS AND CLEANING UP

Remove any foreign material from in and around motor and guards.

Keep the work area and implement shed in a safe, clean and tidy condition.

## POTENTIAL HAZARDS AND INJURIES

Kick-back.

Push-back.

Pull-in.

Rotating chain.

Flying debris.

Trip hazards.

Hair/clothing getting caught in moving machine parts.

Noise.

## DON’T

Do not use faulty equipment.  Report suspect machinery immediately.

Do not use in wet conditions.

Never use a chainsaw over shoulder height

This SWP does not necessarily cover all possible hazards associated with this equipment and should be used in conjunction with other references.  It is designed as a guide to be used to compliment training and as a reminder to users prior to equipment use.

This information is based on material published by the South Australian Department of Education and Children’s Services.